This page was exported from Labappara scientific instrument [    https://www.labappara.com    ]

Export date: Tue Apr 16 5:43:30 2024 / +0000 GMT

# CD / VCD / DVD Disc Player Demonstrator

Product Categories: Audio Visual Lab Demonstrators & Trainers, Audio Visual Lab Demonstrators & Trainers, Electronics, Engineering Equipment

Product Page: https://www.labappara.com/product/color-tv-demonstrator-with-14-crt/

## Product Description

#### CD / VCD / DVD Disc Player Demonstrator

CD / VCD / DVD Player Trainer is designed to provide a live demonstrator of the working of a CD / VCD / DVD Player. The circuit / mechanical assembly is mounted on suitable board for the students to visually observe the electronic circuits and mechanical parts easily. A neat block diagram along with details of test points are provided on charts. Provision is made to measure / observe the voltages and waveforms at various strategic points through sockets.

Technical Specifications:

- Power Supply : 230V AC, 50 Hz, 1phase

- Functions : Play, Pause, Forward, Rewind, Stop, Open, Close, Repeat, Skip and Track select (available on Main Unit and / or Remote)

- Display : Provided

- Laser : Semiconductor laser

- TV System : PAL

- Audio Output : 2.1 Audio System

- Output Socket : Audio out ; Video out

- Input : USB

- CD's Format : Audio, MP3 CD, VCD & DVD

- Remote Control : Multi function remote

- Standard Accessories : Detailed instruction manual, CD (Audio), VCD, DVD, MP3 CD, USB, A/V Cord, Mains Cord and Remote Control

Product added date: 2018-06-30 11:06:16

Product modified date: 2018-06-30 11:16:18

Product export as MS Document by WooCommerce PDF & Print plugin.