This page was exported from Labappara scientific instrument [    https://www.labappara.com    ]

Export date: Thu Apr 18 18:13:30 2024 / +0000 GMT

# Discharge Over Notches

Product Categories: Engineering Equipment, Hydraulic Lab

Product Page: https://www.labappara.com/product/discharge-over-notches-2/

## Product Description

#### Discharge Over Notches

Technical Description:

The setup consists of a channel having sufficient length and width in which water is supplied from the bottom. Required Notch is fitted at one end of this channel. A pointer gauge with Vernier scale is fitted to measure the height of fluid in flow channel. Arrangement for fixing interchangeable notches is made. Set of three notches, i.e. rectangular notch, 60 V notch & 45 V notch is provided along with the set-up. Present set-up is self-contained water re-circulating unit, provided with a sump tank and a centrifugal pump etc. Flow control valve and by-pass valve are fitted in water line to conduct the experiment on different flow rates. Flow rate of water is measured with the help of measuring tank and stopwatch.

Technical Specifications:

- Channel Test Section : Size 600 x 250 x 180 mm.

- Notches : Material Brass

- Rectangular Notch

- 45° V Notch

- 60° V Notch

- Pointer Gauge : With Vernier scale.

- Water Circulation : FHP Pump Crompton make.

- Flow Measurement : Using Measuring Tank with Piezometer, Capacity 25 Ltrs.

- Sump Tank : Capacity 50 Ltrs.

- Stop Watch : Electronic.

- The whole set-up is ingeniously designed and schematically arranged on a powder-coated rigid structure

Product added date: 2018-05-04 11:41:33

Product modified date: 2018-05-10 13:04:49

Product export as MS Document by WooCommerce PDF & Print plugin.