This page was exported from Labappara scientific instrument [    https://www.labappara.com    ]

Export date: Thu Apr 18 12:19:12 2024 / +0000 GMT

# Time Constant Of Thermocouples & Thermometer

Product Categories: Engineering Equipment, Process- Control & Instrumentation Lab

Product Page: https://www.labappara.com/product/time-constant-thermocouples-thermometer/

## Product Description

Technical Description:

The setup consists of a Heat source controlled with the help of digital temperature controller at any preset value. A thermometer/thermo-couple pocket is provided to insert the thermometer/thermo-couple in it.

The time constant of different thermometer/thermo-couple can be calculated with the set-up. A stopwatch is

also provided for measurement of time. A Heat sink is fitted to cool down the thermometer/ thermo-couple. All components are assembled on a base plate to form table top set-up.

LEARNING OBJECTS/EXPERIMENTATION:

To determine time constant of a given thermometer/thermo-couple

REQUIREMENT FOR OPERATION:

Electricity supply : 220 V AC, Single Phase, 0.5 kW.

Ice.

Table for set-up support.

TECHNICAL SPECIFICATION:

- Heat Source : Provided with Ceramic insulation.

- Heater : Ni-chrome Wire Heater.

- Temp. Controller : Digital Temperature controller, 0 to 200°C

- ICE Pot : Compatible capacity.

- Thermometer : Glass Thermometer, Range 0-100°C.

- Thermo-couple : Fe-Constant an type

Instruction Manual : An ENGLISH instruction manual will be provided along

- with the Apparatus

The whole unit is assembled rigidly on a panel plate.

- Most of the parts are powder coated and rests are painted with auto paints.

Product added date: 2018-05-07 12:01:05

Product modified date: 2018-05-11 11:26:12

Product export as MS Document by WooCommerce PDF & Print plugin.